## Slide 1
Human involvement
Table 1/15
Initial question | Potential direction it opens
Who was involved or exposed, and what role did each person have? | Worker, contractor, supervisor, operator, witness, bystander; assigned responsibility, authority, exposure location
What was each person trying to accomplish immediately before the event? | Task objective, competing priorities, production pressure, troubleshooting goal, informal work, mismatch between assigned and actual work
What actions or non-actions are factually established, and what remains assumed? | Verified sequence, decision points, perception, response, omitted action, unreliable reconstruction, premature human-error conclusion
What information, cues, instructions, or warnings were available at the time? | Briefing, alarm, label, signal, visibility, language, comprehension, missing or conflicting information; may activate Communication / supervision
What qualifications, training, authorization, or task familiarity were relevant? | Competency, certification, authorization, contractor qualification, refresher training, unfamiliar or non-routine task
Were fatigue, overtime, workload, physical capability, ergonomics, or time pressure potentially relevant? | Shift length, staffing, workload, fatigue, distraction, reach, force, posture, physical limitation, schedule pressure
What PPE or protective clothing was expected, available, and observed? | PPE selection, availability, condition, fit, compatibility, use, enforcement, hazard assessment
How did the task setup, equipment, environment, or organization shape the person’s available choices? | Equipment design, access, visibility, procedure practicality, supervision, staffing, incentives, line of fire; handoff to the relevant specialist

## Slide 2
Human involvement
Table 1/15
Initial question | Potential direction it opens
Who was involved or exposed, and what role did each person have? | Worker, contractor, supervisor, operator, witness, bystander; assigned responsibility, authority, exposure location
What was each person trying to accomplish immediately before the event? | Task objective, competing priorities, production pressure, troubleshooting goal, informal work, mismatch between assigned and actual work
What actions or non-actions are factually established, and what remains assumed? | Verified sequence, decision points, perception, response, omitted action, unreliable reconstruction, premature human-error conclusion
What information, cues, instructions, or warnings were available at the time? | Briefing, alarm, label, signal, visibility, language, comprehension, missing or conflicting information; may activate Communication / supervision
What qualifications, training, authorization, or task familiarity were relevant? | Competency, certification, authorization, contractor qualification, refresher training, unfamiliar or non-routine task
Were fatigue, overtime, workload, physical capability, ergonomics, or time pressure potentially relevant? | Shift length, staffing, workload, fatigue, distraction, reach, force, posture, physical limitation, schedule pressure
What PPE or protective clothing was expected, available, and observed? | PPE selection, availability, condition, fit, compatibility, use, enforcement, hazard assessment
How did the task setup, equipment, environment, or organization shape the person’s available choices? | Equipment design, access, visibility, procedure practicality, supervision, staffing, incentives, line of fire; handoff to the relevant specialist

## Slide 3
Electrical incident
Table 2/15
Initial question | Potential direction it opens
What electrical asset, circuit, or system could be involved? | Equipment/tool, wiring, panel, battery, controls, temporary power, upstream or downstream circuit
What was the confirmed energy state immediately before and during the event? | Energized work, unexpected energization, stored energy, induced voltage, battery power, unknown or unverified state
What work, interaction, or change was occurring around the electrical system? | Operating, maintenance, testing, troubleshooting, installation, cleaning, switching, physical contact
What evidence suggests an electrical event or abnormal condition? | Shock, arc flash, heat, smoke, tripped device, damaged insulation, exposed conductor, abnormal equipment behavior
What was different from the normal equipment or work condition? | Temporary wiring, outage configuration, bypass, recent repair, damaged component, changed setup, wet or contaminated condition
What protection or control was expected to prevent exposure, and what was its observed state? | Isolation / LOTO, breaker, fuse, relay, interlock, grounding, guarding, PPE; may activate equipment or procedure paths
Who or what could have been exposed, and by what possible path? | Human involvement, direct or indirect contact, conductive path, nearby personnel, contractor exposure, equipment damage
Were surrounding conditions relevant to the electrical exposure or failure? | Work-environment involvement: water, dampness, confined access, poor visibility, conductive surfaces, congestion

## Slide 4
Equipment or tool involvement
Table 3/15
Initial question | Potential direction it opens
What equipment, tool, component, or interface was involved? | Machine, hand tool, power tool, guard, fixture, attachment, structural component, connection or interface boundary
What was it expected to do, and what did it actually do? | Functional deviation, failure to move, unintended movement, drift, release, jam, loss of control, abnormal response
What was its physical and operating condition before and after the event? | Wear, fracture, deformation, corrosion, contamination, overheating, misalignment, damage pattern, latent defect
Was it the correct equipment or tool for the task and conditions? | Selection, suitability, compatibility, capacity, rating, substitute tool, improper application; may activate Procedure / planning
Had it been inspected, maintained, repaired, modified, or reported defective? | Missed inspection, maintenance quality, recurring defect, modification, temporary repair, deferred work, defect reporting
What setup, alignment, guarding, support, clearance, or attachment condition existed? | Installation error, removed guard, temporary support, inadequate restraint, interference, loose attachment, outage configuration
What operating limits, loads, tolerances, or failure modes may be relevant? | Overload, fatigue, tolerance stack-up, design margin, pressure, speed, temperature, foreseeable failure mode
What physical evidence could distinguish failure, misuse, unsuitable design, or external influence? | Fracture surface, witness marks, measurements, logs, testing, photographs, debris, sequence evidence, expert examination

## Slide 5
Mobile equipment / vehicle involvement
Table 4/15
Initial question | Potential direction it opens
What mobile equipment or vehicle was involved, and what task was it performing? | Forklift, loader, truck, trailer, cart, tractor; travel, loading, unloading, towing, parking, positioning
What was its movement, position, speed, load, and direction immediately before the event? | Backing, turning, stopping, acceleration, rollaway, unstable load, blind-side travel, collision sequence
What route, travel surface, clearance, traffic pattern, and exclusion zone existed? | Poor surface, slope, congestion, restricted clearance, traffic-plan weakness, pedestrian separation, route change
What could the operator and nearby people see or hear? | Blind spots, mirrors, cameras, alarms, lighting, noise, obstruction, line of sight, pedestrian awareness
What was the equipment’s condition, including brakes, steering, tires, alarms, lights, restraints, and attachments? | Mechanical failure, missed pre-use inspection, maintenance issue, disabled warning, tire or brake condition, attachment defect
Was the load stable, secured, within capacity, and compatible with the equipment? | Overcapacity, shifted load, poor center of gravity, incorrect attachment, inadequate securement, visibility obstruction
Who controlled or directed the movement, and how was coordination handled? | Operator qualification, spotter, signal, radio, movement authority, conflicting direction; activates Communication / supervision
What changed from the normal route, task, equipment, load, or surrounding activity? | Temporary route, substitute vehicle, unusual load, outage congestion, simultaneous work, changed traffic control

## Slide 6
Crane, lifting, or suspended-load involvement
Table 5/15
Initial question | Potential direction it opens
What lifting equipment, rigging, attachment, and load were involved? | Crane, hoist, sling, hook, magnet, chainfall, lifting beam, attachment point, load identity
What stage of the lift or suspended condition existed at the time? | Rigging, initial take-up, hoisting, travel, rotation, landing, release, parked suspension, residual suspended state
What were the load’s weight, center of gravity, geometry, stability, and attachment points? | Unknown weight, shifting center of gravity, unstable geometry, inadequate pick points, unbalanced or changing load
Were the crane, hoist, rigging, and lifting devices suitable and within rated capacity? | Capacity, load chart, rigging angle, side loading, component compatibility, below-the-hook rating, overload protection
What inspections, condition checks, and lift planning applied? | Pre-use inspection, rigging condition, critical-lift plan, engineering review, missed defect, unsuitable or absent plan
Who operated, rigged, signaled, directed, or worked near the lift? | Operator, rigger, signaler, lift director, qualification, role clarity, positioning; Human involvement
What line-of-fire, exclusion-zone, clearance, swing, or travel conditions existed? | People beneath or near load, pinch point, swing radius, overhead obstruction, wind, congestion, inadequate barricade
What evidence explains any unintended movement, release, contact, shift, or fall? | Rigging failure, attachment release, control input, overload, contact, structural failure, gravity path, event sequence

## Slide 7
Rail / locomotive involvement
Table 6/15
Initial question | Potential direction it opens
What locomotive, rail car, track, switch, derail, or related equipment was involved? | Rolling stock, trackmobile, switch, derail, crossing, coupler, brake, loading or unloading equipment
What movement or rail task was occurring, and what was the intended route? | Switching, coupling, uncoupling, spotting, loading, securement, authorized route, unintended movement
What were the positions and securement states of the rolling stock before the event? | Hand brakes, chocks, air brakes, gradient, uncoupled cars, rollaway, incorrect consist position
What was the condition of the track, switches, derails, brakes, couplers, and warning systems? | Track defect, switch alignment, derail position, brake failure, coupler defect, signal or warning malfunction
Who controlled, authorized, directed, or observed the movement? | Engineer, conductor, ground person, dispatcher, contractor, movement authority, qualification, role clarity
What signals, radio calls, confirmations, or switching instructions were used? | Missed or misunderstood signal, radio failure, readback, confirmation, conflicting instruction; Communication / supervision
What clearance, fouling, crossing, pedestrian, vehicle, or loading conditions existed? | Fouled track, close clearance, crossing conflict, pedestrian exposure, vehicle interaction, loading interference
What changed from the planned consist, route, load, switching sequence, or operating condition? | Route change, added car, unusual load, altered sequence, temporary track condition, maintenance or outage activity

## Slide 8
Stored, released, or gravity energy
Table 7/15
Initial question | Potential direction it opens
What form or forms of energy were present? | Gravity, hydraulic, pneumatic, pressure, spring, tension, thermal, steam, compressed air, mechanical or rotational energy
Where was the energy stored, supported, restrained, or generated? | Raised component, pressure vessel, accumulator, cylinder, line, spring, counterweight, suspended or tensioned object
What prevented the energy from being released during normal conditions? | Support, keeper, pin, brake, valve, block, restraint, interlock, structural member, pressure-control device
What changed immediately before the movement or release? | Removal, loss of pressure, control action, vibration, component failure, contact, temperature change, altered configuration
What object, fluid, component, or person was within the potential energy path? | Line of fire, crush zone, fall zone, pressure discharge, moving component, nearby structure, exposed worker
What blocking, support, restraint, pressure control, or secondary protection existed? | Primary and secondary blocks, cribbing, mechanical stop, check valve, relief device, redundant support, exclusion zone
Was the amount or direction of energy understood and accounted for in the work? | Energy assessment, load or pressure calculation, hidden energy, unexpected direction, incomplete hazard recognition
What physical evidence could identify the release point, sequence, and failure of containment or support? | Damage pattern, fracture, displaced parts, gauge or control records, witness marks, fluid path, photographs, measurements

## Slide 9
Isolation / LOTO involvement
Table 8/15
Initial question | Potential direction it opens
What equipment or system was being isolated, and for what work? | Isolation scope, affected equipment, maintenance boundary, task dependency, wrong or incomplete equipment identification
What hazardous-energy sources and boundaries were identified? | Electrical, hydraulic, pneumatic, gravity, thermal, chemical, mechanical, stored or secondary energy; boundary completeness
What isolation points, locks, tags, blocks, blanks, disconnects, or valves were used? | Correct isolation point, missing device, ineffective valve, wrong disconnect, absent block, lock or tag application
How was zero energy or the intended safe state verified? | Tryout, meter test, pressure check, visual verification, drain or bleed, test-before-touch, assumed rather than verified state
What stored, residual, induced, gravity, or secondary energy remained possible? | Accumulator pressure, trapped fluid, elevated load, induced voltage, spring force, thermal energy, backfeed
Who established, controlled, changed, or relied on the isolation? | Authorized employee, affected employee, contractor, supervisor, system owner, authority, handoff and reliance
Were group, contractor, shift-change, testing, temporary-energization, or restoration conditions involved? | Group lockbox, transfer, turnover, exception, test energization, lock removal, startup and restoration sequence
What evidence confirms the isolation state at each important point in the event sequence? | LOTO sheet, lockbox log, switching record, photographs, meter readings, valve position, witness statement, timestamped state

## Slide 10
Maintenance, outage, or non-routine work
Table 9/15
Initial question | Potential direction it opens
What work was planned, and what was actually being performed? | Planned versus actual scope, emergent work, troubleshooting, informal task, scope drift, conflicting work orders
What equipment, process, or area was placed in a non-normal condition? | Shutdown, opened system, bypass, removed guard, disabled control, isolated area, changed process or access
What had been removed, disabled, bypassed, opened, supported, or temporarily configured? | Missing component, temporary support, defeated interlock, open boundary, abnormal load path, incomplete reassembly
What work occurred on previous shifts or by other crews and contractors? | Shift handoff, incomplete work, changed state, contractor interface, undocumented action, ownership gap
What scope changes, discoveries, delays, or conflicting activities occurred? | Change control, new hazard, schedule pressure, simultaneous operations, work conflict, contingency planning
What condition was the system expected to be left in between work stages? | Interim safe state, temporary configuration, responsibility, tagging, preservation, unattended equipment condition
What inspections, hold points, testing, and return-to-service steps applied? | Missed verification, premature release, incomplete testing, signoff, commissioning, restoration or startup control
What evidence documents the configuration and work sequence? | Work order, outage schedule, shift log, photographs, permits, configuration drawing, contractor record, control-system history

## Slide 11
Process or material involvement
Table 10/15
Initial question | Potential direction it opens
What process and material were involved, and what condition were they expected to be in? | Normal process state, material specification, molten metal, chemical, gas, coil, scrap, fluid, expected containment
What were the actual temperature, pressure, composition, moisture, quantity, shape, or physical state? | Overtemperature, overpressure, contamination, moisture reaction, unstable shape, excess quantity, unexpected phase
What containment, separation, cooling, ventilation, or handling controls applied? | Vessel, piping, barrier, cooling, exhaust, segregation, transfer method, loss of containment or control
What changed in the process or material before the event? | Process excursion, feed change, startup or shutdown, blockage, buildup, contamination, changed recipe or material source
Was the material compatible with the equipment, container, environment, and task? | Chemical incompatibility, unsuitable container, thermal effect, moisture contact, equipment rating, handling mismatch
What signs of leakage, buildup, contamination, reaction, overheating, instability, or loss of containment existed? | Leak path, residue, pressure rise, smoke, discoloration, unusual odor, deformation, unstable load or reaction
What process monitoring, sampling, alarms, inspections, or quality checks were available? | Alarm response, missing instrument, trend data, sampling gap, inspection frequency, out-of-limit condition
What evidence could distinguish a material problem, process excursion, equipment failure, or handling issue? | Samples, lab results, historian data, damage pattern, equipment inspection, batch record, witness account, CCTV

## Slide 12
Work-environment involvement
Table 11/15
Initial question | Potential direction it opens
Where did the event occur, and what physical features of the area were relevant? | Area layout, pit, platform, confined space, aisle, elevation, equipment proximity, restricted or unusual access
Were height, access, openings, ladders, scaffolds, stairs, or changing elevations involved? | Fall exposure, scaffold or ladder condition, open hole, access method, edge protection, elevation transition
What were the walking and working surfaces, housekeeping, drainage, and congestion conditions? | Slip, trip, uneven surface, debris, water, poor drainage, blocked route, material congestion, unstable footing
What lighting, visibility, noise, weather, temperature, or wind conditions existed? | Poor visibility, glare, noise masking, heat or cold stress, rain, ice, wind effect, communication difficulty
Was dust, fume, gas, oxygen level, ventilation, or another atmospheric exposure possible? | Toxic or combustible atmosphere, oxygen deficiency, welding fume, dust, vapor, asbestos, inadequate ventilation
What clearances, barriers, exclusion zones, escape paths, and lines of sight existed? | Line of fire, inadequate barricade, restricted egress, blind area, pinch point, pedestrian or equipment separation
Was the area in its normal condition, or had work, deterioration, or temporary arrangements changed it? | Outage scaffold, temporary barrier, removed floor section, deterioration, construction, maintenance staging, changed access
What photographs, measurements, monitoring results, inspections, or witness observations establish the conditions? | Scene documentation, atmospheric readings, lighting level, dimensions, weather record, inspection, corroborated observations

## Slide 13
Procedure / planning involvement
Table 12/15
Initial question | Potential direction it opens
What work was intended, and what governing procedure, plan, permit, or assessment applied? | Work scope, procedure, JSHA, permit, risk assessment, checklist, undocumented or misclassified work
Did the document match the actual task, equipment, hazards, people, and conditions? | Generic or outdated procedure, wrong asset, omitted hazard, contractor mismatch, field conditions not represented
What critical steps, limits, hold points, prerequisites, and contingencies were defined? | Missing step, unclear limit, absent verification, weak prerequisite, no contingency, uncontrolled decision point
What resources, staffing, time, tools, and information were planned and available? | Understaffing, unavailable tool, insufficient time, missing drawing, skill mix, production pressure, resource conflict
What changes or discoveries occurred, and how were they assessed and authorized? | Scope change, emergent condition, management of change, stop-work, approval, informal workaround
Was the sequence workable, understandable, and consistent with how the job was actually performed? | Impractical sequence, ambiguous instruction, work-as-imagined versus work-as-done, deviation driven by field reality
What known hazards and previous lessons were incorporated? | Repeat event, missed learning, outdated risk assessment, known defect, absent historical control, weak organizational learning
What evidence shows how the plan was briefed, used, revised, or departed from? | Pre-job briefing, signoff, field copy, revision history, permit record, observed practice, deviation or approval trail

## Slide 14
Communication / supervision involvement
Table 13/15
Initial question | Potential direction it opens
Who needed to communicate or coordinate, and for what decision or action? | Crew interfaces, contractor coordination, operator-maintainer boundary, movement authority, isolation or work ownership
What information was sent, received, understood, confirmed, or missing? | Incomplete message, misunderstanding, no readback, missing warning, conflicting information, language or comprehension gap
What communication method was used, and was it suitable for the conditions? | Radio, hand signal, face-to-face instruction, written handoff, noise, visibility, channel failure, unsuitable medium
Who had authority and responsibility for the work, movement, isolation, or area? | Unclear ownership, overlapping authority, absent decision-maker, contractor role, supervisor accountability, stop-work authority
What shift, contractor, department, or crew handoffs occurred? | Turnover quality, changed equipment state, incomplete work, undocumented condition, responsibility transfer
What supervision, verification, or field presence was expected and available? | Span of control, absent supervisor, verification point, remote direction, inadequate field oversight, staffing
Were concerns, changes, conflicts, or abnormal conditions raised and resolved? | Escalation, stop-work, unresolved concern, normalized deviation, production conflict, feedback failure
What records or independent evidence establish the communication sequence? | Shift log, radio recording, text or email, permit, briefing record, witness accounts, timestamped control data

## Slide 15
Animal / wildlife / insect involvement
Table 14/15
Initial question | Potential direction it opens
What animal, wildlife, or insect was involved, and how was it identified? | Species or agent, bite or sting risk, contamination, behavior, mistaken identification, required response
Where and when was it encountered, and was the presence expected or previously reported? | Habitat, seasonal pattern, recurring sighting, prior warning, inspection history, location-specific exposure
What contact, bite, sting, startle, distraction, contamination, or movement occurred? | Direct injury, allergic response, startled movement, loss of balance, distraction, contaminated area or equipment
Were nests, food sources, openings, seasonal conditions, or habitat factors present? | Entry point, nesting site, attractant, housekeeping, vegetation, weather, facility deterioration, pest-management need
What immediate medical, first-aid, containment, or area-control response occurred? | Treatment delay, allergy protocol, emergency response, exclusion zone, containment, decontamination, reporting
What pest-management, inspection, warning, or reporting controls existed? | Preventive inspection, pest contractor, missing warning, reporting pathway, recurring unresolved condition
Did the encounter create a secondary exposure such as a fall, vehicle movement, dropped object, or equipment contact? | Stored energy, mobile equipment, work at height, dropped object, line of fire, unintended machine interaction
What evidence establishes the encounter and its role in the event? | Photograph, specimen, medical finding, witness account, nest or entry point, pest record, scene evidence

## Slide 16
Other / novel condition
Table 15/15
Initial question | Potential direction it opens
What condition or subject is not represented by the existing tags? | Precise definition of the potentially novel direction; prevents Other from becoming a general uncertainty bucket
What facts show that it is materially connected to the event? | Evidence of relevance, temporal connection, mechanism, exposure, consequence; screens out interesting but immaterial details
Which existing tag is closest, and why is it insufficient? | Taxonomy boundary, possible reassignment, overlap, hidden distinction, need for a genuinely separate investigative path
What distinct investigation questions does this condition require? | Unique mechanism, evidence source, subject-matter expertise, control family, causal branch not covered elsewhere
Is it genuinely novel, or is only the wording or specific object unusual? | Synonym resolution, site terminology, unusual equipment still covered by Equipment/tool, avoid unnecessary new tags
Has the same theme appeared in other incidents under different language? | Recurrence, historical pattern, taxonomy normalization, broader category, trend analysis
What evidence could confirm or screen out this direction quickly? | Discriminating test, record, expert review, inspection, measurement, interview, rapid reassignment
Should the condition remain a case-specific note or be proposed for taxonomy review? | One-off condition, recurring gap, new permanent tag candidate, governance and taxonomy-change decision